## Slide 1: Optometric Low Vision
Simple to Complex Solutions to help your clients
Cindy Roles O.D.
Dakota Eye Institute
Bismarck, ND

## Slide 2: Home Vision Assessment Low Vision Distance Acuity
Feinbloom Chart
  Held at 10’ or closer
  Record test distance/letter size
  Example
    If the 3rd row is read at 5 feet
    Acuity is 5/25 or 20/100
    Conversion to 20 feet
5
25
×
4
4
=
20
100

## Slide 3: Home Vision Assessment Near Acuity
Test each eye if you think one eye may be interfering with the other
Helps determine if LV aid should be a monocular or binocular device

## Slide 4: Home Vision Assessment How Does Reading Work?
We think text looks like this:
What our brain actually sees is this:
Try this Exercise:
Keep your fixation on the 7 in the middle of these numbers and see how well you can read the numbers to either side
Notice how hard it is to keep your attention from jumping to the other numbers
This is why eccentric fixation is easier said than done
4569 7 2837
leader
Notes: It doesn’t seem that way, because as soon as we switch our fixation and attention to the next section, our brain creates an integrated composite image that is full of detail

## Slide 5: Home Vision Assessment Scotoma and Reading
Scotoma to right of fixation is significant for reading fluency
Ring Scotoma – may need less magnification
From Patient’s Point of View
  Something is blocking their view
  Letters or words are disappearing and reappearing

## Slide 6: Home Vision Assessment Finding Reading Scotomas
California Central Field Test
  Central 15 degrees
  Sheet at 57 cm (about 2 feet)
  Use laser pointer on the target
Amsler Grid
www.macularsociety.org

## Slide 7: Home Vision Assessment Eccentric Fixation Training Tips
Use pictures - move eye slowly in direction of PRL and pay attention to missing details appearing
Watching the News – finding faces on the TV, picking out features of news readers
Practice with a clock at home
Practice with food on plate
Reading
  Build up from single words to well-spaced words to normal text
  Teach line changing techniques
    Read to end of one line, trace back to beginning of that line, move straight down to the next line
    Use line guides and reading boards

## Slide 8: Home Vision Assessment Contrast Sensitivity
Degree to which one can separate an object from its background
Think about normal vision on a foggy day
Symptoms of poor contrast sensitivity
  Difficulty identifying faces or features in a face
  Trouble reading newsprint
  Difficulty seeing food on a plate (potatoes on white plate)
  Trouble with steps, stairs and curbs
  History of trips and falls
  Vision described as foggy, cloudy & hazy
Two patients with these views may test equally on visual acuity chart but function very differently.
Normal Contrast
Decreased Contrast

## Slide 9: Home Vision Assessment Contrast Sensitivity
Normal Contrast Sensitivity is 2 log units
Moderate impairment is less than 1.5 log units
Severe vision impairment is less than 1 log unit
Pelli-Robson Contrast Sensitivity Chart

## Slide 10: Home Vision Assessment Contrast Sensitivity
Normal Contrast Sensitivity is 2 log units
Moderate impairment is less than 1.5 log units
Severe vision impairment is less than 1 log unit
Berkley Contrast Squares App

## Slide 11: Glare
Defined as: Sensitivity to Light
Not just reflective glare that you see bouncing off a surface
Discomfort glare - Causes pain or discomfort
Disabling Glare
  Impairs function
  Can see a reduction in visual acuity
Blinding Glare
  Impairs function
  Can cause loss of vision for short to extended periods of time
Strategies
  Use filters
  Change or reduce lighting
  Multiple strategies for areas in the home
  Outdoor strategies will be different

## Slide 12: Home Vision Assessment Absorptive Filters – Tint
The sicker the optic nerve,
the yellower the lens
  Glaucoma
  Optic neuritis
  Optic neuropathy
  Optic atrophy
  Optic nerve hypoplasia
  Psuedotumor
Retinal pathology
  Orange, amber, yellow
  AMD
  Diabetic retinopathy
  Achromatopsia
  Retinitis pigmentosa
Concussion, brain injury, migraine
  FL-41
  Dark plum

## Slide 13: Enhance Contrast
Increase Light but limit glare
Move light source
Adjust intensity
Reduce background reflectivity
Use appropriately tinted lenses
Modify figure-ground relationship
Medicine over a black mat
Use a white plate with dark food

## Slide 14: Task Lighting Training
Reduces the required magnification
Light should be at or below eye level
If set above eye level, should be rotated away from eyes
Light should be set off to side so light reflecting off the object doesn’t bounce into user’s eyes
Adjustable Brightness
Inverse Square Rule
  2x as close = 4x as bright
Color Temperature – more for comfort
  Demonstrate different color options to patient
Gooseneck Arm - bend at many angles (to reduce glare)

## Slide 15: Low Tech
Things you can feel
  Bump Dots
  Rubber Bands
  Safety Pins
  Puffy Paint
  Velcro
  Twist Ties
  Sock Locks

## Slide 16: Writing and Typing
Bold Pens & Paper
Paper Guides
Check Guides
Envelope Guides
Signature Guides
Large Print Checks with tactile lines
Large Print keyboard stickers
High contrast keyboard stickers
Not always aligned
Reusable
Cost Effective

## Slide 17: Talking Devices

## Slide 18: ScripTalk
Pharmacy adds a small electronic tag to prescription bottles
Patient places bottle on a little listening station at home
Listening station reads all the information out loud
  Drug Name, dosage, instructions, warnings
  Pharmacy info, Doctor’s name, prescription number
  Can jump forward/back through all the information
ScripTalk Station is provided on loan at no charge by En-Vision America
Option to download a FREE ScripTalk Mobile App from Google Play or the Apple App Store to access their prescription info
www.envisionamerica.com

## Slide 19: Magnifying Devices
Relative Distance Magnification
  Spectacles
Binocular Correction
  Progressives
  Bifocals
  Reading Glasses
  Prism Eyewear
Monocular Correction
  Microscopic Spectacles
Relative Size Magnification
Optical Magnifiers
  Hand-held magnifiers
  Stand magnifiers
Video Magnifiers
Telescopes

## Slide 20: Magnification
Example from Feinbloom Chart
  If the patient read the 3rd row on the chart from 5’ away
  Visual Acuity is 5/25 or 20/100
  If the goal acuity is 20/40
  100 ÷ 40 = 2.5 x magnification needed
How Much Magnification Does My Patient Need?
  Magnification required = Vision achieved
Vision required

## Slide 21: Relative Distance Magnification Reading Glasses
Bringing and object 3x closer makes it 3x larger
Assume normal working distance of 40 cm (about 16 inches)
If the patient can read 2.5M print at 40 cm but wants to read 1M print
The reading material must be moved 2.5x closer
1
0.16
+6.25 diopter
Readers
=
1
Distance in meters
=
Needed Reading Glasses Power
=
Add Power | Working Distance (inches) | Relative Distance Magnif.
+1.00 | 40 | 0.4x
+1.50 | 26 | 0.6x
+2.00 | 20 | 0.8x
+2.50 | 16 | 0
+3.00 | 13 | 1.25x
+3.50 | 11 | 1.45x
+4.00 | 10 | 1.6x
+5.00 | 8 | 2x
+6.00 | 7 | 2.3x
+7.00 | 6 | 2.7x
+10.00 | 4 | 4x
+12.50 | 3 | 5x
40
2.5
=
16 cm (about 6 inches)
Needed Working Distance
=

## Slide 22: Near Magnification Dispensing Reading Glasses
Ensure required print size, lighting and contrast
Put the reading glasses on the patient and have them read at the required distance
  Make sure they will be comfortable with that distance
Hint: Cut straw or pipe cleaner to the appropriate working distance and give it to the patient to use to keep at the needed distance
Base in Prism – will be needed in higher power reading glasses to support the high amount convergence at close distances
  Usually higher than +4.00 needs BI prism
Add Power | Working Distance (inches) | Relative Distance Magnif.
+1.00 | 40 | 0.4x
+1.50 | 26 | 0.6x
+2.00 | 20 | 0.8x
+2.50 | 16 | 0
+3.00 | 13 | 1.25x
+3.50 | 11 | 1.45x
+4.00 | 10 | 1.6x
+5.00 | 8 | 2x
+6.00 | 7 | 2.3x
+7.00 | 6 | 2.7x
+10.00 | 4 | 4x
+12.50 | 3 | 5x

## Slide 23: Spectacle Magnifiers
Binocular viewing
  Prism eyewear
  Diffractive eyewear
  Reading glasses
Familiar
Hands-free
Wide field of view
Inconspicuous
Short working distance
Conspicuous
Not Illuminated
Advantages
Disadvantages
Monocular Viewing
  Microscopic spectacles
  Diffractive microscopic spectacles

## Slide 24: Hand-Held Magnifiers
A Strong Plus Lens and a Handle
1X Magnification = 4 Diopters
  ANSI Standard
Familiar
Versatile
Economical
Portable
Not Hands-free
Fatiguing
Stronger powers – Smaller lens
Advantages
Disadvantages

## Slide 25: Rules for Using Hand-Held Magnifiers
Hold Lens Parallel to the object being viewed
Hold the lens at its focal length
Hold lens at proper eye to lens distance (as labeled on the magnifier)
Mag | Diopters | Lens Size | Lens to object | Eye to lens
3x | 12 | 2.4" | 2" | 10"
3.5x | 10 | 2"x3" | 2" | 10"
4x | 16 | 2"x3" | 1.75" | 6"
4x | 16 | 2.4" | 1.4" | 6"
5x | 20 | 2.4" | 1.2" | 5"
6x | 24 | 2.4" | 1.2" | 4"
7x | 28 | 1.4" | 1.2" | 2"
10x | 38 | 1.4" | .8" | 2"
12.5x | 50 | 1.2" | .6" | 2"
Magnification
Diopters
Eye to Lens Distance
140 mm = 1.2”

## Slide 26: Stand Magnifiers
Plus Lens mounted on “legs” that fix the distance from lens to object
Fixed focal length
Lens mounted parallel to object
Great for reading
Less fatiguing
Not hands-free
Less portable
Limited field of view
Advantages
Disadvantages

## Slide 27: Rules for Using Stand Magnifiers
Hold the stand magnifier firmly against the object to be viewed
Adjust eye to lens distance appropriately
Divergent light rays emerge from Stand Magnifier lenses.
Users must accommodate or wear a bifocal
System VarioPlus |  | 
Mag | Lens Size | Eye to Lens
3x | 2" x 4" | 10"
3.9x | 2" x 4" | 8"
3x | 3.2" | 10"
4x | 2.8" | 6"
5x | 2.4" | 5"
6x | 2" | 4"
7x | 1.4" | 2"
10x | 1.4" | 2"
12.5x | 1.2" | 2"

## Slide 28: Video magnifiers
An electronic device that magnifies by using a camera that projects an enlarged image on a screen or monitor
Equivalent Power
  Screen magnification x accommodation
  Add power multiplies the magnification effect

## Slide 29: Video Magnifier for Distance Viewing
Video Magnifier for Distance Viewing

## Slide 30: Telescopes
Hand-Held
  Spotting Tasks
Eyeglass Mounted
  Extended Viewing (TV & Reading)
  Driving
Multiple Task Solution
Long working distance at near
Hands-Free
Distance Magnification
Conspicuous
Loss of peripheral field / field of view
Heavy for longer term wear
Advantages
Disadvantages

## Slide 31: Telescopes

## Slide 32: Custom-Mount Telescopic Glasses
Inferior Mount for Reading
Superior Mount for Distance Spotting
Full Field Mount for Long-term Viewing
Bioptics
Custom-Mount Telescopic Glasses
Bioptics

## Slide 33: Smart Phone Apps
Magnification Apps & Smartphone Adaptations
Visor - iOS & Android
Install magnifier on iOS or Android phone
Super Vision + -iOS & Android
Adjust Color & Brightness on iOS or Android phone
Text to Speech Apps & Voice Assistants
Seeing AI – iOS
Google Lookout -Android
Sullivan + -iOS & Android
Hey Google –Android
Envision AI-Android
Siri- iOS
Bixby- Android
Google Assistant -Android & iOS

## Slide 34: Smart Phone Apps
Live person Assistance Apps
Be My Eyes -iOS & Android - free
AIRA iOS & Android
  costs $ but free trial
Object Identifier Apps
TapTapSee- iOS & Android
  need to turn on voice over
WayAround- Tag & Scan- iOS
  need to purchase tags
Money Reader Apps
Cash Reader - iOS & Android
Seeing AI – iOS
EyeNote – iOS
Blind-Droid Wallet – Android
Darwin Wallet – Android
IDEAL Currency Identifier - Android

## Slide 35: Windows Computer Accessibility
Set up “Ease of Access”
In Windows XP & Windows 7
  Found in the control panel
In Windows 8 and Windows 10
  Found in the App section
Ease of Access Features
Change the contrast of the display to 4 different high-contrast
Change the size and color of the mouse cursor.
Open a floating magnifier that enlarges part of the screen
  Easily access this feature by pressing the Windows "Start" button on the keyboard and "+".
Key combination
  "Crtl +" to zoom in
  "Crtl -" to zoom out
  Can also roll mouse wheel forward or back
Ease of Access Features
Change the default font to a clearer font such as Arial or Verdana
Change the size of the scroll bars and window borders
Change the size of the desktop icons from normal to large to extra large.

## Slide 36: Windows Computer Accessibility
Change Email Settings
Microsoft Outlook
  Changes font, font size, and font color
  Applied to all incoming and outgoing emails
  Found in Options under the File dropdown menu
  Always set the default font to a clear, easy to read font such as Arial or Verdana.
Internet Settings
Web browsers (Internet Explorer, Google Chrome, Mozilla Firefox, Safari, etc.) have the option to change the default font and font size
Extensions are available from third-party companies that add special features to your web browser
Found under your web browser's Settings and they include:
  Menus with easy access to most-visited websites and bookmarked pages
  Changes in menu designs, colors, and fonts
  Applications such as large clocks, calendars, note pads, calculators, and many more

## Slide 37
Thank You